1.5km UAV Jammer LCD Display 5 Band 900MHz

2.4G,2.4G, 1.5G,5.8G Drone Signal Jammer

Model.UAV108

With drone sales expected grow exponentially in the near future, and an increasing number and severity of drone incidents occurring daily, We launched Drone jammer Gun to respond to nefarious use of consumer and commercial drones and the resulting need for effective countermeasures to drone intrusions. Drone jammer gun aims to help public and private sector customers, where allowed by law, take proactive measures against airborne threats to safety, security, and privacy.
Portable light Drone Jammer, Built-in high gain directional antenna, Built 5 sets of independently operated RF working unit, can choose to on/off GPS to drive the drone or force the drone to land, can be transmitted shielding interference signals to the surrounding 25-degree angle, jamming range (1200-1500m) can be comprehensive and stable uninterrupted shielding of the 900MHz, GPSL1, GPSL2, WIFI 2.4G, 433MHz, 5.2G and 5.8G bands in the UAV frequency band.

Feature:

1. Replaceable battery design, operating time 50-60 minutes,

2. Higher gain antenna 15dBi

3. Strong jamming range, 1200-1500meters

4. Inner cooling fan design, Device work continuously

5. Split modular design.

Antenna & Main unit can assemble/disassemble easily.

6. The split design is easy for clearance at customs.

7. 16 x telescope, Anti-vibration, Easy to spot and target drones

Product Description:

Type A:  2.4G, 2.4G, 5.8G, GPSL1, 900MHz

Type B:  2.4G, 5.2G, 5.8G, GPSL1, 900MHz

Type C:  2.4G, 5.2G, 5.8G, GPSL1, GPSL2, 900MHz

Type D:  2.4G, 5.8G, GPSL1, 900MHz, GPSL2, 433MHz

Type E:  2.4G, 2.4G, 5.8G, 5.8G, GPSL1, 900MHz

Type F:  2.4G, 5.2G, 5.8G, GPSL1,900MHz,433MHz

Type G:  900MHz, 2.4G, 5.2G, 5.8G, GPSL1, GPSL2, 433MHz

| Channel | Working Frequency | Output power(±1.5dBm) |
| --- | --- | --- |
| CH1 | 2.4G | 2400-2485MHz | 45 dBm |
| CH2 | 2.4G | 2400-2485MHz | 45 dBm |
| CH3 | 5.8G | 5725-5850MHz | 44 dBm |
| CH4 | GPSL1 | 1560-1620MHZ | 45 dBm |
| CH5 | 900MHz | 860-930MHz | 41 dBm |
| Power supply mode | Inside battery: 24V, 8.5A; Or External battery |
| Battery working time | 40-50 minutes |
| Working temperature | -20ºC to +55ºC |
| Total Output Power | 125W |
| Power consumption | 250W |
| Weight | 7.3KG, Package Weight: 22KG |
| Size | 830X370X240mm |
| Directional Antenna | 15dBi Gain |